## Slide 1: Network management
Basic Networking
- what’s happening on my network ?! 

## Slide 2: Network management
Network management is the general term for control and monitoring of all network units and users.
  The devices can be: routers, hubs, switches, servers, workstations etc.
Control and monitoring of devices means:
  Remote control (for example, configuring routers or servers).
  Automatic installation and uninstallation of software.
  Hardware and software inventories and queries.
  Status and error messages from the devices.

## Slide 3: Why network management?
Reasons for the great interest in network management:
  For companies today, it has become like “The network is the business!”
  Almost all services, functions and production controls is carried through the network
  Many networks of today is too complex to be monitored manually, and demands the use of management software to ensure a stable operation
  The ability to outsource the operation of a complete network
  There is money to be saved with a well functioning network management
  https://en.wikipedia.org/wiki/Network_management
  http://www.solarwinds.com/basics-of-network-monitoring.aspx

## Slide 4: SNMP and CMIP
For a network management system can work with devices from different manufacturers, it is important to have some management standards that manufacturers can implement in their products
The two main standards are:
  SNMP (Simple Network Management Protocol )
    An IETF ( Internet Engineering Task Force ) protocol.
    IETF standardize protocols for the Internet
    SNMP is the most widely used Network Management Protocol
  CMIP (Common Management Information Protocol )
    An OSI Network Management Protocol , which is designed to monitor and control the network.

## Slide 5: SNMP - overview and history
SNMP is designed so that network devices can exchange management information
SNMP ( Simple Network Management Protocol ) is an application layer protocol, but are in principle located at the network layer and above
SNMP was developed in 1988 to facilitate the work with the management and monitoring of routers on the Internet
The reason to develop a new protocol was that the data supporting protocol on the Internet , TCP / IP suite contains management tools for routers
The manufacturers of network devices then quickly implemented SNMP in many of their networking products, and today almost all network devices are available with SNMP
SNMP was in 1989 adopted as a standard in the TCP / IP protocol suite

## Slide 6: SNMP units
Router
Switch
Server
NMS
Network Management System
MIB
Agent
MIB
Agent
MIB
Agent
Polling, Traps and
Get, Set kommandoer
MIB
SNMP managed network systems consists of two types of units:
  Network Management Station (NMS)
  Controlled units (SNMP agents)
NMS (Network Management Station) is usually a PC management software installed.
From NMS you can manage and monitor the individual network devices.
NMS can send commands and receive responses and traps (alarms) from SNMP agents

## Slide 7: SNMP units
Router
Switch
Server
NMS
Network Management System
MIB
Agent
MIB
Agent
MIB
Agent
Polling, Traps and
Get, Set kommandoer
MIB
An SNMP agent is a piece of network management software installed in a controlled device, for example, switch, router or server.
Agents respond to inquiries from NMS, witch means the agent retrieves management information from the device MIB and translates it to SNMP format.
Agents can also receive commands from NMS on changes to be made in the MIB

## Slide 8: Network Management Software
Network management software are programs that can control and monitor network devices. The programs may be proprietary ie that they only work with units of the manufacturer or they may be generic and work with all types of products.
After the development of the protocols SNMP and RMON, it has been possible to make general programs that can control and monitor all the products as long as they use SNMP / RMON.
Network Management station is usually a PC using Linux, Unix or Windows operating system
Examples of popular network management programs are:
  HP OpenView, Nagios, Zenoss
http://ipinfo.info/html/network_management_software.php

## Slide 9: SNMP commands
Management console and network device communicate using SNMP command set
  The philosophy is that there should be few and very simple commands, as the chart below also shows
So if you need a variable from a device such as uptime you’ll send the "Get request variable" command
  The device then sends "Get response variable value"
Send an alert if a specified event (event) occurs
Trap
Save a value in the specified variable
Set – request
Answer to a "Get req." Or "Get next req." Command
Get – response
Get the value of the next variable - after Get request
Get – next request
Get the value of the specified variable
Get – request
Function
SNMP command

## Slide 10: SNMP commands (continued)
Things are different if you have a variable value which has no variable name
  Here it may be necessary to use a "Get request" command and then a number of "Get next request" commands until you find the value.
  It is therefore SNMP can provide much traffic on the network
It is also possible to set a threshold value (threshold) into a variable, for example, to alert if traffic exceeds 90% of max. capacity
  This means that the device sends a Trap message to the management console if the value is exceeded
Send an alert if a specified event (event) occurs
Trap
Save a value in the specified variable
Set – request
Answer to a "Get req." Or "Get next req." Command
Get – response
Get the value of the next variable - after Get request
Get – next request
Get the value of the specified variable
Get – request
Function
SNMP command

## Slide 11: SNMP commands (continued)
Communication between the Network Manager station and the SNMP agent takes place with application layer protocol SNMP (Simple Network Management Protocol).
SNMP uses the UDP transport protocol and uses ports 161-162 to exchange messages.
NMS
Network Management System
MIB
SNMP controlled Router
GetRequest, GetNextRequest, SetRequest
GetResponse, Trap
Send an alert if a specified event (event) occurs
Trap
Save a value in the specified variable
Set – request
Answer to a "Get req." Or "Get next req." Command
Get – response
Get the value of the next variable - after Get request
Get – next request
Get the value of the specified variable
Get – request
Function
SNMP command

## Slide 12: SNMP versions
SNMP comes in three major versions:
  SNMP v1, v2 & v3
Developments from SNMP v1 to v2 contains three major changes:
  GetBulkRequest command can retrieve all the data from the MIB at once, instead of using the inefficient "GetRequest" command and then a number of "GetNextRequest" commands until you find the value
  64-bit counters in the MIB rather than 32-bit counters
  Trap command (send an alarm if a specified event occurs)

## Slide 13: SNMP versions (continued)
Developments from SNMP v1-2 to v3 is mostly on security issues:
  SNMP v1 and v2 uses only community strings (SNMP community name) in clear text authentication (qualifying).
  Remember to change the default community strings as SNMP agents and NMS installed with
    Read-only agent access: public
    Read-write access agent: private
  SNMP v3 allows for secure communication between the NMS and the agent MIB through access control and encryption.
The following is possible with SNMP v3:
  Username Password-like
  Access control based on MD5 (Message Digest algorithm 5)
  Access control based on MD5 and encryption using DES (Data Encryption Standard)

## Slide 14: MIB - Management Information Base
In network devices are placed a database containing information about the device itself
The database is called MIB (Management Information Base) and is structured as a tree structure as described in the SMI (Structure of Management Information)
Below “Root” in the tree on the next slide there are 3 branches, managed respectively by ISO and CCITT (ITU-T) and one that’s administered by both organizations

## Slide 15: MIB tree
Cisco
D-Link
Fore
IBM
Enterprise(1)
?
?
HP
Event(9)
Statistics(1)
History(2)
Alarm(3)
Hosts(4)
Hosts Top N(5)
Matrix(6)
Token Ring(10)
Filter(7)
Capture(8)
RMON I
MIB II (1)
IP(4)
Transm.(10)
TCP(6)
AT(3)
CMOT(9)
UDP(7)
EGP(8)
ICMP(5)
Interfaces(2)
System (1)
User History(18)
Probe Configuration(19)
RMON II
RMON Conformance(20)
Application-Layer Matrix(17)
Application-Layer Host(16)
Network-Layer Matrix(15)
Network-Layer Host(14)
Address Mapping(13)
Protocol Distribution(12)
Protocol Directory(11)
ORG(3)
DoD(6)
ISO(1)
Management(2)
Directory(1)
Eksperimental(3)
Private(4)
Internet(1)
RMON(2)
Root
CCITT(2)
ISO/CCITT(3)
Below DOD we find the Internet and this is where SNMP is located
The “address” of the Internet is (1.3.6.1).
Two branches are interesting in management purposes, namely Management and Private.
Company stuff!
Company stuff!
Company stuff!
Standards!

## Slide 16: MIB variants
MIB are divided into 8 groups with a total of 114 standard objects.
MIB II expands MIB I to 185 objects divided into 11 groups.
RMON I and II are standard MIBs for Remote Monitoring.
In addition to these MIBs, there are many manufacturer MIBs
SNMP info
SNMP
11
Support for fx Token Ring, Ethernet højhastighed, FDDI osv.
Transmission
10
Common Management information protocol Over Tcp/ip
CMOT
9
Exterior Gateway Protocol software
EGP
8
User Datagram Protocol software
UDP
7
Transmission Control Protocol software
TCP
6
Internet Control Message Protocol software
ICMP
5
Internet Protocol software
IP
4
Address translation eg. ARP
Addr. Translation
3
Connections
Interfaces
2
System description, uptime, name, location, services, object ID
System
1
Descriptions
MIB II categories

## Slide 17: RMON (Remote Monitoring)
Remote Network Monitoring (RMON) is an extension of SNMP
RMON defines some intelligent agents / probes that can tell when something happens management console should know
  It is a MIB that collects network statistics by analyzing packets on the network
  RMON 1 is described in RFC 1757 -1513 (Ethernet / Token Ring)
  RMON 2 is described in RFC 2021 and 2074
  RMON 1 is placed in the OSI-model's IOS 1-2 RMON and bottom layer 2 in the layers 3-7
OSI-model
7. Applikation
6. Præsentation
5. Session SNMP RMON 2
4. Transport
3. Netværk
2. Datalink RMON 1
1. Fysisk

## Slide 18: RMON I categories
Collecting data from Token Ring-based network
Token Ring
10
Steer send SNMP Traps to remote clients (manage consol)
Events
9
Collect and store selected data packets
Packet capture
8
Can filter data packets so you only see certain data packets
Filter
7
Trace data traffic between two systems
Traffic matrix
6
The probe can sort host information from specific statistical data
Host top N
5
Can find new devices on the network if a new MAC addr. shows
Hosts
4
Used for alarm if one of the two threshold values (up / down) is reached
Alarm thresholds
3
History sets of Statistics (1) for comparison and trend analysis
History sets
2
Collection of network traffic, eg. broadcast, unicast, errors …
Statistics
1
Description
RMON 1 categories

## Slide 19: RMON II categories
RMON Conformance
20
Standard for remote configuration of the probe parameters such as Trap destination
Probe Configuration
19
Periodic measurements of the user specify the variable
User History
18
Traffic statistic to and from each host using. Protocols up to the application protocol
Application-Layer Matrix
17
Trafik statistik til og fra hver host vha. protokoller op til applikations protokol
Network-Layer Host
16
Traffic statistics between host couple
Network-Layer Matrix
15
Traffic statistic to and from each host
Network-Layer Host
14
Mapping Network Layer addr. to the MAC layer addr. Facilitates analysis of data
Address Mapping
13
Traffic statistics for each protocol such as IPX, IP etc.
Protocol Distribution
12
Showing what protocols a probe can monitor. Used by Network Management Station
Protocol Directory
11
Description
RMON 2 categories